## Slide 1
<footer>
<date/time>
Chapter 4 Combinational logic circuit DESign

## Slide 2
4.1 Gate Circuit
two feed nonequality gate
logical symbol

## Slide 3
behave OF xor2_v1
LIBRARY IEEE;
USE IEEE.STD_LOGIC_1164.ALL;
ENTITY xor2_v1 IS
PORT(a,b: IN STD_LOGIC;
y: OUT STD_LOGIC);
END xor2_v1;
ARCHITECTURE behave OF xor2_v1 IS
BEGIN
y <= a XOR b;
END behave;
a b y
0 0 0
0 1 1
1 0 1
1 1 0
truth table

## Slide 4
dataflow OF xor2_v2
LIBRARY IEEE;
USE IEEE.STD_LOGIC_1164.ALL;
ENTITY xor2_v2 IS
PORT(a,b: IN STD_LOGIC;
y: OUT STD_LOGIC);
END xor2_v2;
ARCHITECTURE dataflow OF xor2_v2 IS
BEGIN
PROCESS (a,b)
VARIABLE comb : STD_LOGIC_VECTOR(1 DOWNTO 0);
BEGIN
comb := a & b;

## Slide 5
CASE comb IS
WHEN "00"=> y <='0';
WHEN "01"=> y <='1';
WHEN "10"=> y <='1';
WHEN "11"=> y <='0';
WHEN OTHERS => y <='X';
END CASE;
END PROCESS;
END dataflow;

## Slide 6
simulation waveform

## Slide 7
4.2 Encoder
I
I
I
I
I
I
I
I
0
1
3
2
4
5
6
7
A
A
A
0
1
2
8line-3line
encoder

## Slide 8
I0 I1 I2 I3 I4 I5 I6 I7 A2 A1 A0
0 0 0 0 0 0 0 0 0 0
0 1 0 0 0 0 0 0 0 0 1
0 0 1 0 0 0 0 0 0 1 0
0 0 0 1 0 0 0 0 0 1 1
0 0 0 0 1 0 0 0 1 0 0
0 0 0 0 0 1 0 0 1 0 1
0 0 0 0 0 0 1 0 1 1 0
0 0 0 0 0 0 0 1 1 1 1
Truth table
input output

## Slide 9
logical expression：
A2=I4+I5+I6+I7
A1=I2+I3+I6+I7
A0=I1+I3+I5+I7
behave OF coder83_v1
LIBRARY IEEE;
USE IEEE.STD_LOGIC_1164.ALL;
ENTITY coder83_v1 IS
PORT(I0,I1,I2,I3,I4,I5,I6,I7: IN STD_LOGIC;
A0,A1,A2: OUT STD_LOGIC);
END coder83_v1;
ARCHITECTURE behave OF coder83_v1 IS
BEGIN

## Slide 10
A2 <= I4 OR I5 OR I6 OR I7;
A1 <= I2 OR I3 OR I6 OR I7;
A0 <= I1 OR I3 OR I5 OR I7;
END behave;

## Slide 11
simulation waveform

## Slide 12
dataflow OF coder83_v2
LIBRARY IEEE;
USE IEEE.STD_LOGIC_1164.ALL;
ENTITY coder83_v2 IS
PORT( I: IN STD_LOGIC_VECTOR(7 DOWNTO 0);
A: OUT STD_LOGIC_VECTOR(2 DOWNTO 0));
END coder83_v2;
ARCHITECTURE dataflow OF coder83_v2 IS
BEGIN
PROCESS (I)
BEGIN

## Slide 13
CASE I IS
WHEN "10000000"=> A <="111";
WHEN "01000000"=> A <="110";
WHEN "00100000"=> A <="101";
WHEN "00010000"=> A <="100";
WHEN "00001000"=> A <="011";
WHEN "00000100"=> A <="010";
WHEN "00000010"=> A <="001";
WHEN OTHERS => A <="000";
END CASE;
END PROCESS;
END dataflow;

## Slide 14
simulation waveform

## Slide 15
4.3 Priority encoder
1
Priority encoder
I
I
7
I
6
I
I
0
I
I
I
8line-3line
4
3
2
5
74148
GS
EO
A
A
2
1
A
0
EI

## Slide 16
EI I0 I1 I2 I3 I4 I5 I6 I7 A2 A1 A0 GS EO
1 × × × × × × × × 1 1 1 1 1
0 1 1 1 1 1 1 1 1 1 1 1 1 0
0 × × × × × × × 0 0 0 0 0 1
0 × × × × × × 0 1 0 0 1 0 1
0 × × × × × 0 1 1 0 1 0 0 1
0 × × × × 0 1 1 1 0 1 1 0 1
0 × × × 0 1 1 1 1 1 0 0 0 1
0 × × 0 1 1 1 1 1 1 0 1 0 1
0 × 0 1 1 1 1 1 1 1 1 0 0 1
0 0 1 1 1 1 1 1 1 1 1 1 0 1
input output
Truth table

## Slide 17
logical expression

## Slide 19
LIBRARY IEEE;
USE IEEE.STD_LOGIC_1164.ALL;
ENTITY prioritycoder83_v1 IS
PORT(I7,I6,I5,I4,I3,I2,I1,I0 : IN STD_LOGIC;
EI:IN STD_LOGIC;
A2,A1,A0: OUT STD_LOGIC;
GS,EO:OUT STD_LOGIC);
END prioritycoder83_v1;
ARCHITECTURE behave OF prioritycoder83_v1 IS
BEGIN
A2 <= EI OR (I7 AND I6 AND I5 AND I4);
A1 <= EI OR (I7 AND I6 AND I3 AND I2)
OR (I7 AND I6 AND NOT I5)
OR (I7 AND I6 AND NOT I4) ;
behave OF prioritycoder83_v1

## Slide 20
A0 <= EI OR (I7 AND NOT I6)
OR (I7 AND I5 AND NOT I4)
OR (I7 AND I5 AND I3 AND I1)
OR (I7 AND I5 AND I3 AND NOT I2);
GS <= EI OR (I7 AND I6 AND I5 AND I4 AND I3
AND I2 AND I1 AND I0);
EO <= EI OR NOT(I7 AND I6 AND I5
AND I4 AND I3 AND I2 AND I1 AND I0);
END behave;

## Slide 21
simulation waveform

## Slide 22
Note：This is illegal：
WHEN “0XXXXXXX”=>A<=“000”；
LIBRARY IEEE;
USE IEEE.STD_LOGIC_1164.ALL;
ENTITY prioritycoder83_v2 IS
PORT ( I: IN STD_LOGIC_VECTOR(7 DOWNTO 0);
EI:IN STD_LOGIC;
A: OUT STD_LOGIC_VECTOR(2 DOWNTO 0);
GS,EO:OUT STD_LOGIC);
END prioritycoder83_v2;

## Slide 23
ARCHITECTURE dataflow OF prioritycoder83_v2 IS
BEGIN
PROCESS(EI,I)
BEGIN
IF(EI='1')THEN
A <= "111";
GS <= '1';
EO <= '1';
ELSIF (I="11111111" AND EI='0')THEN
A <= "111";
GS <= '1';
EO <= '0';

## Slide 24
ELSIF (I(7)='0' AND EI='0')THEN
A <= "000";
GS <= '0';
EO <= '1';
ELSIF (I(6)='0' AND EI='0')THEN
A <= "001";
GS <= '0';
EO <= '1';
ELSIF (I(5)='0' AND EI='0')THEN
A <= "010";
GS <= '0';
EO <= '1';

## Slide 25
ELSIF (I(4)='0' AND EI='0')THEN
A <= "011";
GS <= '0';
EO <= '1';
ELSIF (I(3)='0' AND EI='0')THEN
A <= "100";
GS <= '0';
EO <= '1';
ELSIF (I(2)='0' AND EI='0')THEN
A <= "101";
GS <= '0';
EO <= '1';

## Slide 26
ELSIF (I(1)='0' AND EI='0')THEN
A <= "110";
GS <= '0';
EO <= '1';
ELSE (I(0)='0' AND EI='0')THEN
A <= "111";
GS <= '0';
EO <= '1';
END IF;
END PROCESS;
END dataflow;

## Slide 27
simulation waveform

## Slide 28
5.4 Decoder
decoder
3-8LINE
74138
0
A
A
1
A
2
G
1
G
G
2A
2B
2
7
Y
4
0
Y
1
Y
Y
Y
Y
Y
Y
6
5
3

## Slide 29
G1 G2A G2B A2 A1 A0 Y0 Y1 Y2 Y3 Y4 Y5 Y6 Y7
× 1 × × × × 1 1 1 1 1 1 1 1
× × 1 × × × 1 1 1 1 1 1 1 1
0 × × × × × 1 1 1 1 1 1 1 1
1 0 0 0 0 0 0 1 1 1 1 1 1 1
1 0 0 0 0 1 1 0 1 1 1 1 1 1
1 0 0 0 1 0 1 1 0 1 1 1 1 1
1 0 0 0 1 1 1 1 1 0 1 1 1 1
1 0 0 1 0 0 1 1 1 1 0 1 1 1
1 0 0 1 0 1 1 1 1 1 1 0 1 1
1 0 0 1 1 0 1 1 1 1 1 1 0 1
1 0 0 1 1 1 1 1 1 1 1 1 1 0
INPUT OUPUT
Truth table

## Slide 30
dataflow OF decoder138_v2
LIBRARY IEEE;
USE IEEE.STD_LOGIC_1164.ALL;
ENTITY decoder138_v2 IS
PORT(G1,G2A,G2B: IN STD_LOGIC;
A: IN STD_LOGIC_VECTOR(2 DOWNTO 0);
Y: OUT STD_LOGIC_VECTOR(7 DOWNTO 0));
END decoder138_v2;
ARCHITECTURE dataflow OF decoder138_v2 IS
BEGIN
PROCESS (G1,G2A,G2B,A)
BEGIN
IF(G1='1' AND G2A='0' AND G2B='0')THEN

## Slide 31
CASE A IS
WHEN "000" => Y <="11111110";
WHEN "001" => Y <="11111101";
WHEN "010" => Y <="11111011";
WHEN "011" => Y <="11110111";
WHEN "100" => Y <="11101111";
WHEN "101" => Y <="11011111";
WHEN "110" => Y <="10111111";
WHEN OTHERS => Y <="01111111";
END CASE;
ELSE Y <="11111111";
END IF;
END PROCESS;
ENDdataflow;

## Slide 32
simulation waveform

## Slide 33
5.5 Multichannel data selector
D
G
0
D
D
1
Y
D
74151
3
D
D
Y
5
D
4
2
7
6
D
1
0
A
A
2
A

## Slide 34
enable address Y Y b
G A2 A1 A0
1 × × × 0 1
0 0 0 0 D0 D0
0 0 0 1 D1 D1
0 0 1 0 D2 D2
0 0 1 1 D3 D3
0 1 0 0 D4 D4
0 1 0 1 D5 D5
0 1 1 0 D6 D6
0 1 1 1 D7 D7
input output
Truth table

## Slide 35
dataflow OF mux8_v2
LIBRARY IEEE;
USE IEEE.STD_LOGIC_1164.ALL;
ENTITY mux8_v2 IS
PORT(A: IN STD_LOGIC_VECTOR (2 DOWNTO 0);
D0,D1,D2,D3,D4,D5,D6,D7:IN STD_LOGIC;
G:IN STD_LOGIC;
Y: OUT STD_LOGIC;
YB:OUT STD_LOGIC);
END mux8_v2;
ARCHITECTURE dataflow OF mux8_v2 IS
BEGIN
PROCESS (A,D0,D1,D2,D3,D4,D5,D6,D7,G)

## Slide 36
BEGIN
IF (G ='1') THEN
Y <='0';
YB <='1';
ELSIF(G='0'AND A="000")THEN
Y <= D0;
YB <= NOT D0;
ELSIF(G='0'AND A="001")THEN
Y <= D1;
YB <= NOT D1;
ELSIF(G='0'AND A="010")THEN
Y <= D2;
YB <= NOT D2;

## Slide 37
ELSIF(G='0'AND A="011")THEN
Y <= D3;
YB <= NOT D3;
ELSIF(G='0'AND A="100")THEN
Y <= D4;
YB <= NOT D4;
ELSIF(G='0'AND A="101")THEN
Y <= D5;
YB <= NOT D5;
ELSIF(G='0'AND A="110")THEN
Y <= D6;
YB <= NOT D6;

## Slide 38
ELSE
Y <= D7;
YB <= NOT D7;
END IF;
END PROCESS;
END dataflow;

## Slide 39
simulation waveform

## Slide 40
CASE statement
LIBRARY IEEE;
USE IEEE.STD_LOGIC_1164.ALL;
ENTITY mux8_v3 IS
PORT(A2,A1,A0: IN STD_LOGIC;
D0,D1,D2,D3,D4,D5,D6,D7:IN STD_LOGIC;
G:IN STD_LOGIC;
Y: OUT STD_LOGIC;
YB:OUT STD_LOGIC);
END mux8_v3;
ARCHITECTURE dataflow OF mux8_v3 IS
SIGNAL comb: STD_LOGIC_VECTOR(3 DOWNTO 0);

## Slide 41
BEGIN
comb <= G & A2 & A1 & A0;
PROCESS (comb,D0,D1,D2,D3,D4,D5,D6,D7,G)
BEGIN
CASE comb IS
WHEN "0000" =>
Y <= D0;
YB <= NOT D0;
WHEN "0001" =>
Y <= D1;
YB <= NOT D1;
WHEN "0010" =>
Y <= D2;
YB <= NOT D2;

## Slide 42
WHEN "0011" =>
Y <= D3;
YB <= NOT D3;
WHEN "0100" =>
Y <= D4;
YB <= NOT D4;
WHEN "0101" =>
Y <= D5;
YB <= NOT D5;
WHEN "0110" =>
Y <= D6;
YB <= NOT D6;

## Slide 43
WHEN "0111" =>
Y <= D7;
YB <= NOT D7;
WHEN OTHERS =>
Y <='0';
YB <='1';
END CASE;
END PROCESS;
END dataflow;

## Slide 44
simulation waveform

## Slide 45
5.6 Numeric comparator
Example
compare two 4_bit(A、B）：
if A>B then YA=1,
if A<B then YB=1,
if A=B then YC=1,

## Slide 46
LIBRARY IEEE;
USE IEEE.STD_LOGIC_1164.ALL;
ENTITY comp4_v1 IS
PORT(A:IN STD_LOGIC_VECTOR(3 DOWNTO 0);
B:IN STD_LOGIC_VECTOR(3 DOWNTO 0);
YA,YB,YC: OUT STD_LOGIC);
END comp4_v1;
ARCHITECTURE behave OF comp4_v1 IS
BEGIN
PROCESS (A,B)
BEGIN
IF (A > B) THEN
YA <='1';
YB <='0';
YC <='0';

## Slide 47
ELSIF(A < B) THEN
YA <='0';
YB <='1';
YC <='0';
ELSE
YA <='0';
YB <='0';
YC <='1';
END IF;
END PROCESS;
END behave;

## Slide 48
simulation waveform

## Slide 49
5.7 Adder
A 、B，Cin，S，Co
Truth table
A B CI | CO F
0 0 0 0 0 1 0 1 0 0 1 1 1 0 0 1 0 1 1 1 0 1 1 1 | 0 0 0 1 0 1 1 0 0 1 1 0 1 0 1 1

## Slide 50
LIBRARY IEEE;
USE IEEE.STD_LOGIC_1164.ALL;
USE IEEE.STD_LOGIC_UNSIGNED.ALL;
ENTITY adder8_v IS
PORT(A :IN STD_LOGIC_VECTOR(7 DOWNTO 0);
B :IN STD_LOGIC_VECTOR(7 DOWNTO 0);
Cin:IN STD_LOGIC;
Co : OUT STD_LOGIC;
S :OUT STD_LOGIC_VECTOR(7 DOWNTO 0));
END adder8_v;
ARCHITECTURE behave OF adder8_v IS
SIGNAL Sint : STD_LOGIC_VECTOR(8 DOWNTO 0);
SIGNAL AA,BB: STD_LOGIC_VECTOR(8 DOWNTO 0);

## Slide 51
BEGIN
AA <='0'& A(7 DOWNTO 0);
BB <='0'& B(7 DOWNTO 0);
Sint <= AA + BB + Cin;
S(7 DOWNTO 0) <= Sint(7 DOWNTO 0);
Co <= Sint(8);
END behave;

## Slide 52
simulation waveform