## Slide 1
CHAPTER 2 vhdl language element

## Slide 2
（Ⅰ）Object in VHDL
（Ⅱ）Data type in VHDL
（Ⅲ）Operation actor in VHDL

## Slide 3: （Ⅰ）Object in VHDL
Object ： be used to keep data
1、 CONSTANT
2、 SIGNAL
3、 VARIABLE

## Slide 4: Object’ active zone
1、Global in object
Object is declared in package or entity。
2、Partial in object
Object is declared in architecture 。

## Slide 5: 1、 CONSTANT
CONSTANT: value in projet don‘t change
Format:
CONSTANT name：data type[：=expression]；
For example:
CONSTANT pi : REAL :=3.14;
CONSTANT Fbus : BIT_VECTOR := “1011”；
Constant can be evaluated one time and the value should be accord with the defined data type。Evaluate symbol is“：=”。

## Slide 6: 1、 CONSTANT
Defining one constant is primarily in order to make some volume easy to read AND modify
constant’ active zone
1、when constant is declared in package or entity, constant is global.
2、when constant is declared in architecture or process, constant is partial 。

## Slide 7: 2、signal
Signal can be abstracted as hardware connection in circuit, correspond one connecting wire of hardware design。
Format:
SIGNAL name ： data type[：=expression]；
For example:
SIGNAL reset : = STD_LOGIC : =’1’;
SIGNAL data ：STD_LOGIC_VECTOR (7 DOWNTO 0);
Signal can be seriesly evaluated and the value should be accord with the defined data type。Evaluate symbol is“<=”。

## Slide 8: 2、signal
Valuation of signal is not effective immediately, there are a certain time delay。
when signal is declared in package or entity, signal is global.
when signal is declared in architecture, signal is partial 。

## Slide 9: 3、 VARIABLE
Variable is mostly used in local storage for the present data.it is a partial volume，only in process statement, procedure statement and function statement。
Format:
VARIABLE name： data type[：=expression]；
VARIABLE enable := STD_LOGIC;
Variable can be seriesly evaluated and the value should be accord with the defined data type。Evaluate symbol is“:=”。

## Slide 10: 3、 VARIABLE
Valuation of variable is effective immediately and it is poetical data transmission。
variable is declared in process、 procedure or function.

## Slide 11: Example
LIBRARY IEEE;
USE IEEE.STD_LOGIC_1164.ALL;
USE IEEE.STD_LOGIC_UNSIGNED.ALL;
ENTITY example IS
PORT(clk : IN STD_LOGIC;
q : OUT STD_LOGIC);
END example;
ARCHITECTURE a OF example IS
SIGNAL temp : STD_LOGIC_VECTOR(0 TO 2);
BEGIN
count: PROCESS (clk)
VARIABLE counter: STD_LOGIC_VECTOR(0 TO 2):="000";
BEGIN
IF (clk'EVENT AND clk='1') THEN
counter:=counter+'1';
END IF;
temp<=counter;
END PROCESS;

## Slide 12
output: PROCESS (temp)
BEGIN
IF(temp="111") THEN
q<='1';
ELSE
q<='0';
END IF;
END PROCESS;
END a;
Example

## Slide 13: （Ⅱ）DATA TYPE OF VHDL
1、Every object only can have single data type, and only can possess the value of the data type；
2、Operational type must match the type of object；
3、VHDL does not allow direct operations (arithmetic,logical,etc.)between data of different types；
4、when the data types are same whereas bit lengths are different, direct operations are not allowed 。

## Slide 14: （Ⅱ）DATA TYPE OF VHDL
1、INTEGER:32-bit
integers(from -2,147,483,647 to
2,147,483,647
CONSTANT max :INTEGER :=128;
SIGNAL num:INTEGER RANGE 0 TO 100;
VARIABLE f:INTEGER RANGE 6 TO 9;

## Slide 15: 2、REAL
Real numbers ranging from
-1.0E38~+1.0E38。
CONSTANT max :REAL :=128.0;
SIGNAL num: REAL RANGE 0.0 TO 1.0E2;
VARIABLE f:REAL RANGE 6.0 TO 9.0;

## Slide 16: 3、BIT
BIT :2-levellogic(‘0’,‘1’).
SIGNAL tmp:BIT:=’0’;
SIGNAL x : BIT;
-- x is declared as a one-digit signal of type BIT.

## Slide 17: 4、BIT_VECTOR
tmp:BIT_VECTOR(0 TO1):=“01”
SIGNAL s1：BIT_VECTOR（15 DOWNTO 0）；
BIT_VECTOR :2-level logic (‘0’,‘1’).
SIGNAL w : BIT_VECTOR (0TO7);

## Slide 18
5、BOOLEAN
TRUE、FALSE

## Slide 19
6、CHARACTER：
Character literals: Single ASCII character of such characters. Not synthesizable.
CHARACTER（ ‘ 1’）

## Slide 20
7、STRING：
string literals: ASCII characters of such characters. Not synthesizable.
VATIABLE string_1 : STRING (0 TO 3);
┇
string_1:= “a b c d”;

## Slide 21: 8、 Physical literals
20 μs，100 ns，3 sec。
Used to inform physical quantities,like time , voltage, etc . Useful In simulations . Not synthesizable.

## Slide 22
9、SEVERITY LEVEL：
note，warning，error，failure

## Slide 23
10、NATURAL
Non-negative integers (from 0 to +2,147,483,647).

## Slide 24
11、 STD_LOGIC
STD_LOGIC_VECTOR :
9-valued logic system introduced in The IEEE 1164 standard.
‘U’ initial value
‘X’ Forcing Unknown(synthesizable unknown)
‘0’ Forcing Low(synthesizable logic ‘1’)
‘1’ Forcing High(synthesizable logic ‘0’)
‘Z’ High impedance(synthesizable tri-state buffer)
‘W’ Weak unknown
‘L’ Weak low
‘H’ Weak high
‘–’ Don’t care

## Slide 25
SIGNAL x:STD_LOGIC;
--x is declared as a one-digit (scalar) signal of type STD_LOGIC.
SIGNAL y: STD_LOGIC_VECTOR (3 DOWNTO 0):= "0001";
--y is declared as a 4-bit vector, with the left most bit being the MSB. The initial value (optional)of y is "0001".Notice that the ":=“ operator is used to establish the initial value.

## Slide 26
Such data type defnitions can be found in the following packages/libraries:
Package standard of library std :
Defines BIT,BOOLEAN,INTEGER,andREAL datat ypes.
Package std_logic_1164 of library ieee:
Defines STD_LOGIC and STD_ULOGIC data types.
Package std_logic_arith of library ieee:
Defines SIGNED and UNSIGNED datatypes
.
Packages std_logic_signed and std_logic_unsigned
of library ieee

## Slide 27: User-Defined Data Types
VHDL also allows the user to define his/her own data types.
TYPE integer IS RANGE -2147483647 TO +2147483647;
-- This is indeed the pre-defined type INTEGER.
TYPE natural IS RANGE 0 TO +2147483647;
-- This is indeed the pre-defined type NATURAL.

## Slide 28
TYPE my_integer IS RANGE -32 TO 32;
-- A user-defined subset of integers.
TYPE bit IS ('0', '1');
-- This is indeed the pre-defined type BIT
TYPE my_logic IS ('0', '1', 'Z');
-- A user-defined subset of std_logic.

## Slide 29: Subtypes
The main reason for using a subtype rather than specifying a new type is that, though operations between data of different types are not allowed, they are allowed between a subtype and its corresponding base type.

## Slide 30
SUBTYPE my_logic IS STD_LOGIC RANGE '0' TO 'Z';
--Recall that STD_LOGIC=('X','0','1','Z','W','L','H','-').
--Therefore, my_logic=('0','1','Z').
SUBTYPE small_integer IS INTEGER RANGE -32 TO 32;
-- A subtype of INTEGER.

## Slide 31
Example: Legal and illegal operations between types and subtypes.
SUBTYPE my_logic IS STD_LOGIC RANGE '0' TO '1';
SIGNAL a: BIT;
SIGNAL b: STD_LOGIC;
SIGNAL c: my_logic;
...
b <= a; --illegal (type mismatch: BIT versus STD_LOGIC)
b <= c; --legal (same "base" type: STD_LOGIC)

## Slide 32: Data Conversion
VHDL does not allow direct operations (arithmetic, logical, etc.) between data of different types. Therefore, it is often necessary to convert data from one type to another.
This can be done in basically two ways: or we write a piece of VHDL code for that, or we invoke a FUNCTION from a pre-defined PACKAGE which is capable of doing it for us.

## Slide 33
function
STD_LOGIC_1164
TO_STD_LOGIC_VECTOR(A)
TO_BIT_VECTOR(A)
TO_STD_LOGIC (A)
TO_BIT(A)
Convert BIT_VECTOR to STD_LOGIC_VECTOR
Convert STD_LOGIC_VECTOR to BIT_VECTOR
Convert BIT to STD_LOGIC
Convert STD_LOGIC to BIT
STD_LOGIC_ARITH
CONV_STD_LOGIC_VECTOR(A,bit length)
CONV_INTEGER(A)
Convert INTEGER、UNSIGNED、SIGNED to STD_LOGIC_VECTOR
Convert UNSIGNED、SIGNED to INTEGER
STD_LOGIC_UNSIGN
CONV_INTEGER(A)
Convert STD_LOGIC to INTEGER

## Slide 34
Example: Data conversion.
LIBRARY ieee;
USE ieee.std_logic_1164.all; USE ieee.std_logic_arith.all;
...
SIGNAL a: IN UNSIGNED (7 DOWNTO 0);
SIGNAL b: IN UNSIGNED (7 DOWNTO 0);
SIGNAL y: OUT STD_LOGIC_VECTOR (7 DOWNTO 0);
...
y<= CONV_STD_LOGIC_VECTOR ((a+b), 8);
--Legal operation: a+b is converted from UNSIGNED --8-bit STD_LOGIC_VECTOR value, then assigned to to y.

## Slide 35
LIBRARY ieee;
USE ieee.std_logic_1164.ALL;
USE ieee.std_logic_unsigned.ALL;
ENTITY sel1in4 IS
PORT(a: IN STD_LOGIC_VECTOR(1 downto 0);
d: IN STD_LOGIC_VECTOR(3 downto 0);
f: OUT STD_LOGIC);
END sel1in4;
ARCHITECTURE sel OF sel1in4 IS
BEGIN
f<=d(conv_integer(a));
END sel;

## Slide 36
Synthesizable data types.
Data types Synthesizable values
BIT, BIT_VECTOR ‘0’, ‘1’
STD_LOGIC, STD_LOGIC_VECTOR ‘X’, ‘0’, ‘1’, ‘Z’
STD_ULOGIC, STD_ULOGIC_VECTOR ‘X’, ‘0’, ‘1’, ‘Z’ BOOLEAN True, False
NATURAL From 0 to 2, 147, 483, 647
INTEGER From -2,147,483,647 to +2,147,483,647
SIGNED From -2,147,483,647 to +2,147,483,647
UNSIGNED From 0 to 2, 147, 483, 647
User-defined integer type
SUBTYPE Subset of any type (pre-or user-defined)

## Slide 37: （Ⅲ）Operators
（1）Assignment Operators
Are used to assign values to signals, variables, and constants. They are:
<=Used to assign a value to a SIGNAL.
:=Used to assign a value to a VARIABLE, CONSTANT, or GENERIC. Used
also for establishing initial values.
=> Used to assign values to individual vector elements or with OTHERS.

## Slide 38
Example: Consider the following signal and variable declarations:
SIGNAL x : STD_LOGIC;
VARIABLE y : STD_LOGIC_VECTOR(3 DOWNTO 0);
SIGNAL w: STD_LOGIC_VECTOR(0 TO 7);
Then the following assignments are legal:
x <= '1'; -- '1' is assigned to SIGNAL x using "<="
y := "0000"; -- "0000" is assigned to VARIABLE y using ":="
w <= "10000000"; -- LSB is '1', the others are '0'
w <= (0 =>'1', OTHERS =>'0'); -- LSB is '1', the others are '0'

## Slide 39: （Ⅲ）Operators
（2）Logical Operators
Used to perform logical operations. The data must be of type BIT, STD_LOGIC,or STD_ULOGIC (BIT_VECTOR, STD_LOGIC_VECTOR, or STD_ULOGIC_VECTOR) The logical operators are:
NOT、AND、OR、NAND、NOR、XOR、XNOR
Notes: The NOT operator has precedence over the others. The XNOR operator was
introduced in VHDL93.

## Slide 40: Examples: y <= NOT a AND b; -- (a'.b) y <= NOT (a AND b); -- (a.b)' y <= a NAND b; -- (a.b)'

## Slide 41: (3)Arithmetic Operators Used to perform arithmetic operations. The data can be of type INTEGER, SIGNED, UNSIGNED, or REAL. Also, if the std_logic_signed or the std_logic_unsigned package of the ieee library is used, then STD_LOGIC_VECTOR can also be employed directly in addition and subtraction operations
+ — * /
MOD REM ** ABS

## Slide 42: （4）Comparison Operators
Used for making comparisons. The data can be of any of the types listed above. The relational (comparison) operators are:
=Equal to
/=Not equal to
< Less than
> Greater than
<=Less than or equal to
>=Greater than or equal to

## Slide 43: （5）Shift Operators
sll Shift left logic – positions on the right are filled with ‘0’s
srl Shift right logic – positions on the left are filled with ‘0’s
ROL
ROR

## Slide 44: &
SIGNAL g，h，i：STD_LOGIC；
SIGNAL c，d，e：STD_LOGIC _VECTOR（1 TO 0）；
┇
d <= i & NOT h；
a <= c & d；

## Slide 45
The pre-defined, synthesizable data attributes are the following:
d’LOW: Returns lower array index
d’HIGH: Returns upper array index
d’LEFT: Returns leftmost array index
d’RIGHT: Returns rightmost array index
d’LENGTH: Returns vector size
d’RANGE: Returns vector range
d’REVERSE_RANGE: Returns vector range in reverse order
（Ⅳ）Data Attributes

## Slide 46
Example: Consider the following signal:
SIGNAL d : STD_LOGIC_VECTOR (7 DOWNTO 0);
Then:
d'LOW=0, d'HIGH=7, d'LEFT=7,
d'RIGHT=0, d'LENGTH=8,
d'RANGE=(7 downto 0),
d'REVERSE_RANGE=(0 to 7).

## Slide 47
Example: Consider the following signal:
SIGNAL x: STD_LOGIC_VECTOR (0 TO 7);
Then all four LOOP statements below are synthesizable and equivalent.
FOR i IN RANGE (0 TO 7) LOOP ...
FOR i IN x'RANGE LOOP ...
FOR i IN RANGE (x'LOW TO x'HIGH) LOOP ...
FOR i IN RANGE (0 TO x'LENGTH-1) LOOP ...

## Slide 48
Let us consider a signal s. Then:
s’EVENT: Returns true when an event occurs on s
s’STABLE: Returns true if no event has occurred on s
s’ACTIVE: Returns true if s =‘1’
s’QUIET <time>: Returns true if no event has occurred during the time specified
s’LAST_EVENT: Returns the time elapsed since last event
s’LAST_ACTIVE: Returns the time elapsed since last s =‘1’
s’LAST_VALUE: Returns the value of s before the last event; etc.
（Ⅴ）Signal Attributes

## Slide 49
Example: All four assignments shown below are synthesizable and equivalent. They return TRUE when an event (a change) occurs on clk, AND if such event is upward(in other words, when a rising edge occurs on clk).
IF (clk'EVENT AND clk='1')... -- EVENT attribute used
-- with IF
IF (NOT clk'STABLE AND clk='1')... -- STABLE
attribute used
-- with IF
WAIT UNTIL (clk'EVENT AND clk='1') ... -- EVENT
attribute used
- with WAIT
IF RISING_EDGE(clk)... -- call to a function