## Slide 1
CHAPTER1 VHDL Terms

## Slide 2: NOTE
VHDL IS One Language of Hardware Description

## Slide 3: Prescription
（1） Large Alphabetic has no Difference with small Alphabetic .(except ‘A’ ‘a’ “AAA” “aaa”)
（2）Eend attribute with "；"
（3） Comment line begin with "--"

## Slide 4: Prescription
（4） Title rule：
①Title is formed of alpha 、digital and underline；
②The first character must be alpha；
③The last character can not be underline；
④ The title can not be vhdl ‘key words。

## Slide 5: Ⅰ、The Basic structure of VHDL
Exemple:1 bit full adder’vhdl description
ENTITY adder IS
PORT( a, b,cin : IN BIT;
s ,co : OUT BIT);
END adder;
ARCHITECTURE a OF adder IS
BEGIN
s<=a XOR b XOR cin;
co<=((a XOR b) AND cin) OR (a AND b);
END a;
entity
A VHDL entity specifies the name of the entity, the ports of the entity, and entity-related information.
architecture describes the behavior and structure of entity
architecture

## Slide 6: （1） (Entity)
1、Entity
ENTITY <name> IS
[generic parameter description]
[port description]
END < entity name >;
ENTITY adder IS
PORT(
a, b, cin : IN BIT;
s ,co : OUT BIT);
END adder;
Notice：entity begin with statement " ENTITY name IS " ， end with statement " END name；"

## Slide 7: （1）Entity
2、The name of the entity: The name must be same with the disk filename in the software of MAXPLUSII。
ENTITY adder IS
PORT(
a, b, cin : IN BIT;
s ,co : OUT BIT);
END adder;

## Slide 8: （1）Entity
3、Generic parameter description
Generic parameter is one entity description option，lies before description port.it is used to specify entity parameter, such as define port width、device retardation time etc. the general format is：
GENERIC
（constant’name：data type:= setting value；
……
constant’name ：data type:= setting value)；

## Slide 9
Example：
GENERIC （trise，tfall：TIME:=1ns;
addrwidth:INTEGER:=16);
PORT(a0, a1 : IN STD_LOGIC;
Add_bus:OUT STD_LOGIC_VECTOR
(addrwidth-1 DOWNTO 0);
Trise is the width of rising edge ，tfall is the width of falling edge ， used in the design of simulation； Addrwidth is the width of address bus。

## Slide 10: （1）Entity
4、port description
port description describes title、mode、 data type of port.
port : every input and output signal inentity， correspond to one feet of circuit or chip.

## Slide 11: port description
port name : the identification character of the port
Example:Clk、Data、Address
PORT（ port name： port mode data type ；
┇
port name ： port mode data type ）；
port mode : declare the direction of port signal
port mode has several types ： IN、OUT、INOUT、BUFFER

## Slide 12: port mode
① IN
② OUT
③ INOUT
④ BUFFER

## Slide 13: port mode
1．IN
permit signal enter entity，mostly used in input control clock input、 control input （such as load、 reset、 enable、 clk）and unidirectional data input（such as address、 signal）etc.

## Slide 14: port mode
2．OUT
only permit signal quit entity，used in count output、 single direct data output、signals of ConTRoL other entity etc
notice：out mode can not be used to interior signal feedback

## Slide 15: port mode
3．INOUT
enable signal bidirectional transmission （as well as can enter entity，and quit entity），allow interior feedback.

## Slide 16: port mode
4．BUFFER
enabling signal output to entity exterior，along with it can be used at the entity interior. it can be used in output as well as be used in feedback.

## Slide 17: port mode
port mode can be declared by the fllow chart ，the box represents one DESign entity or module.

## Slide 18: Defference of Out and buffer
OUT
BUFFER

## Slide 19: Defference of Out and buffer
Entity test1 is
port(a: in std_logic;
b,c: out std_logic );
end test1;
architecture a of test1 is
begin
b <= not(a);
c <= b;--Error
end a;
Entity test2 is
port(a: in std_logic;
b : buffer std_logic;
c: out std_logic );
end test2;
architecture a of test2 is
begin
b <= not(a);
c <= b;
end a;

## Slide 20
Input signal is defined as “in”，
output signal is defined as “out”，
two-direction data communication signal is defined as “inout” 。

## Slide 21: Data type
Descripte data type of the signal。
VHDL is a kind of tyed language， with 10 kinds of standard data type， can also include self-defining data style by user.
BIT（ ‘0’or‘1’ ） is VHDL ' predefined type， don’t need special explanation when use this style。
when use non- predefined data type，we must use call statement of library AND package 。

## Slide 22: （2） library AND package
LIBRARY IEEE;
USE IEEE.STD_LOGIC_1164.ALL;
ENTITY adder IS
PORT( a, b,cin : IN STD_LOGIC;
s ,co : OUT STD_LOGIC);
END adder;
STD_LOGIC is frequently used ，advisabile value with (‘U’, ‘X’, ‘0’,‘1’ ‘Z’, ‘W’, ‘L’’ ‘H’和 ‘-’ )。

## Slide 23: （2） library AND package
LIBRARY
library is the gather after compiling data，it includes package gather definition、 entity definition、 architecture definition AND configuration definition

## Slide 24: （2） library AND package
“USE” statement points package in library 。
library statement’ format： LIBRARY name；

## Slide 25: （2） library AND package
“USE” statement has two type：
USE library’name.package’name.item’name; USE library’name.package’name.ALL;

## Slide 26: （二）库和程序包
For example： LIBRARY IEEE； USE IEEE.STD_LOGIC_1164.ALL; USE IEEE.STD_LOGIC_1164.STD_ULOGIC;
STD_LOGIC_1164
STD_ULOGIC

## Slide 27
notice：library’ active zone begins with entity and ends with architicture and CONFIGURATION。
example：LIBRARY IEEE； --library define
USE IEEE.STD_LOGIC_1164.ALL;
ENTITY and IS
┇
END and；
ARCHITECTURE dataflow OF and IS
┇
END dataflow;

## Slide 28
CONFIGURATION c1 OF and IS -- CONFIGURATION ┇
AND c1;
LIBRARY IEEE； -- library define
USE IEEE.STD_LOGIC_1164.ALL;
ENTITY or IS
CONFIGURATION c2 OF and IS
┇
AND c2;

## Slide 29: （2） library AND package
library type：
IEEE library 。Package:STD_LOGIC_1164、
STD_LOGIC_ARITH、
STD_LOGIC_UNSIGNED
STD library 。VHDL’ standard library 。
ASIC vector library 。
WORK library 。
user-defined library

## Slide 30: （2） library AND package
Package：mostly be used to store commonly shared data type、subprogram declaration、attribute specification AND component declaration etc for every projet。
“USE” statement 。
Package format：
PACKAGE name IS
[declaration]; PACKAGE head
END name;
PACKAGE BODY name IS
[body contents]； PACKAGE BODY
END BODY;

## Slide 31: （二）库和程序包
example：package ofthree level logic
PACKAGE logic IS
TYPE three_level_logic IS (’0’,’1’,’Z’);
CONSTANT unknown_value: three_level_logic :=’0’;
FUNCTION invert (input : three_level_logic)
RETURN three_level_logic;
END logic;
PACKAGE BODY logic IS
FUNCTION invert (input : hree_level_logic)
RETURN hree_level_logic IS
BEGIN
CASE input IS
WHEN ’0’=> RETURN ’1’;
WHEN ’1’=> RETURN ’0’;
WHEN ’Z’=> RETURN ’Z’;
END CASE;
END invert;
END BODY;

## Slide 32: （3） ARCHITECTURE
The architecture describes the underlying functionality of the entity and contains the statements that model the behavior of the entity. An architecture is always related to an entity and describes the behavior of that entity.
behavior
dataflow
structure

## Slide 33: （3） ARCHITECTURE
ARCHITECTURE must follow the entity 。
ARCHITECTURE format：
ARCHITECTURE <name> OF <entity‘name> IS
[declaration]；
BEGIN
<functional description statement>；
END name;

## Slide 34: （3） ARCHITECTURE
ENTITY adder IS
PORT( a, b,cin : IN BIT;
s ,co : OUT BIT);
END adder;
ARCHITECTURE example OF adder IS
BEGIN
s<=a XOR b XOR cin;
co<=((a XOR b) AND cin) OR (a AND b);
END a;

## Slide 35: （3） ARCHITECTURE
Architecture’name：such as behavior、
Dataflow、structure 。
declaration ： declare the signal、
the constant、 data type、function；
functional description statement ： descripte the behave and structure of Architecture，include Sequential statement and Parallel statement 。
object

## Slide 36
example: data selector
ENTTITY mux2 IS
PORT （d0， sel ，d1：IN BIT；
S ：OUT BIT）；
END mux2；
ARCHITECTURE dataflow OF mux2 IS
SIGNAL sig：BIT；
BEGIN
Sig <= (d0 AND sel) OR (NOT sel AND d1)；
S<=sig；
END dataflow；

## Slide 37
例: data selector
ENTTITY mux2 IS
PORT （d0， sel ，d1：IN BIT；
S ：OUT BIT）；
END mux2；
ARCHITECTURE dataflow OF mux2 IS
SIGNAL sig：BIT；
BEGIN
Sig <= (d0 AND sel) OR (NOT sel AND d1)；
S<=sig；
END dataflow；
Architecture’name
Entity’name
Signal declaration
functional description statement

## Slide 38: （4） CONFIGURATION
CONFIGURATION format：
CONFIGURATION name OF entity’name IS
FOR name
END FOR
END name ；

## Slide 39
example：and、or、nand、nor、xor，5 architecture use 1 entity
LIBRARY IEEE;
USE IEEE.STD_LOGIC_1164.ALL;
ENTITY example_v IS
PORT (a : IN STD_LOGIC;
b : IN STD_LOGIC;
y : OUT STD_LOGIC);
END example_v;
ARCHITECTURE and2_arc OF example_v IS
BEGIN
y <= a AND b;
END and2_arc;

## Slide 40
ARCHITECTURE or2_arc OF example_v IS
BEGIN
y <= a OR b;
END or2_arc;
ARCHITECTURE nand2_arc OF example_v IS
BEGIN
y <= NOT(a AND b);
END nand2_arc;
ARCHITECTURE nor2_arc OF example_v IS
BEGIN
y <= NOT(a OR b);
END nor2_arc;

## Slide 41
ARCHITECTURE xor2_arc OF example_v IS
BEGIN
y <= a XOR b;
END xor2_arc;
CONFIGURATION cfg1 OF example_v IS
FOR and2_arc
END FOR;
END cfg1;
CONFIGURATION cfg2 OF example_v IS
FOR or2_arc
END FOR;
END cfg2;

## Slide 42
CONFIGURATION cfg3 OF example_v IS
FOR nand2_arc
END FOR;
END cfg3;
CONFIGURATION cfg4 OF example_v IS
FOR nor2_arc
END FOR;
END cfg4;
CONFIGURATION cfg5 OF example_v IS
FOR xor2_arc
END FOR;
END cfg5;

## Slide 43
xor simulation waveform

## Slide 44: VHDL program structure
1、Library
2、Package
3、Entity
4、Architecture
5、Configuration

## Slide 45: Ⅱ、 Four description mode of architecture
1、 behavior mode
2、 dataflow mode
3、 structure mode
4、 mixed mode

## Slide 46: 1、 behavior mode
example: 1 bit full adder
LIBRARY IEEE;
USE IEEE.STD_LOGIC_1164.ALL;
ENTITY adder IS
PORT( a, b,cin : IN BIT;
s ,co : OUT BIT);
END adder;
ARCHITECTURE behavior OF adder IS
SIGNAL i : BIT_VECTOR(2 DOWNTO 0);
BEGIN
i<=a&b&cin;
Define inside signal

## Slide 47: 1、 behavior mode
PROCESS(a,b,cin)
BEGIN
CASE i IS
WHEN "000" =>s<='0'; co<='0';
WHEN "001" =>s<='1'; co<='0';
WHEN "010" =>s<='1'; co<='0';
WHEN "011" =>s<='0'; co<='1';
WHEN "100" =>s<='1'; co<='0';
WHEN "101" =>s<='0'; co<='1';
WHEN "110" =>s<='0'; co<='1';
WHEN OTHERS => s<='1'; co<='1'; END CASE;
END PROCESS ;
END behavior;

## Slide 48: 1、 behavior mode
behavior mode is a mathematical model
advantage：don’t care gate level realization。
disadvantage：sometimes cannot go on logic synthesis or has difficulty with syntheses

## Slide 49: 2、dataflow mode
ARCHITECTURE dataflow OF adder IS
SIGNAL tmp1,tmp2 : BIT;
BEGIN
tmp1<=a XOR b;
s<=tmp1 XOR cin; tmp2<=tmp1 AND cin;
co<=tmp2 OR (a AND b);
END dataflow;

## Slide 50: 2、dataflow mode
dataflow mode is the description of signal to signal ' data flow。
advantage：easy to synthesis 。
disadvantage：require user realize the design circuit

## Slide 51: 3、structure mode
ARCHITECTURE structure OF adder IS
COMPONENT and_2
PORT( i1, i2 : IN BIT;
y1 : OUT BIT);
END COMPONENT;
COMPONENT or_2
PORT( i3, i4 : IN BIT;
y2 : OUT BIT);
END COMPONENT;
COMPONENT xor_2
PORT( a, b : IN BIT;
c : OUT BIT);
END COMPONENT;
COMPONENT declaration

## Slide 52: 3、 structure mode
SIGNAL tmp1,tmp2,tmp3 : BIT;
BEGIN
u1: xor_2 PORT MAP (a,b,tmp1);
u2: xor_2 PORT MAP (tmp1,cin,s);
u3: and_2 PORT MAP (tmp1,cin,tmp2);
u4: and_2 PORT MAP (a,b,tmp3);
u5:or_2 PORT MAP (tmp2,tmp3,co);
END structure;
calls component or designed module in library。
advantage： apply available result in current projet and advance design efficiency。

## Slide 53: component
ENTITY and_2 IS
PORT( i1, i2 : IN BIT;
y1 : OUT BIT);
END and_2;
ARCHITECTURE a OF and_2 IS
BEGIN
y1<=i1 AND i2;
END a;
ENTITY or_2 IS
PORT( i3, i4 : IN BIT;
y2 : OUT BIT);
END or_2;
ARCHITECTURE a OF or_2 IS
BEGIN
y2<=i3 OR i4;
END a;
ENTITY xor_2 IS
PORT( i5, i6 : IN BIT;
y3 : OUT BIT);
END xor_2;
ARCHITECTURE a OF xor_2 IS
BEGIN
c<=a XOR b;
END a;
and_2
or_2
xor_2

## Slide 54: 4、 mixed mode
ARCHITECTURE mixed OF add4 IS
COMPONENT or_2
PORT( i3, i4 : IN STD_LOGIC;
y2 : OUT STD_LOGIC);
END COMPONENT;
COMPONENT xor_2
PORT( a, b : IN STD_LOGIC;
c : OUT STD_LOGIC);
END COMPONENT;

## Slide 55: 4、 mixed mode
SIGNAL tmp1,tmp2,tmp3 : STD_LOGIC;
BEGIN
tmp3<=a AND b;
tmp2<=tmp1 AND cin;
u1: xor_2 PORT MAP (a,b,tmp1);
u2: xor_2 PORT MAP (tmp1,cin,s);
u3: or_2 PORT MAP (tmp2,tmp3,co);
END mixed;

## Slide 56: Ⅲ 、 three substructures of architecture
（ⅰ）BLOCK
（ⅱ）SUBPROGRAM
1、PROCEDURE
2、FUNCTION
（ⅲ）PROCESS

## Slide 57: （ ⅰ ）BLOCK
BLOCK structure：
label：BLOCK
interface description
generic declaration
BEGIN
parallel block statement
END BLOCK（label）；

## Slide 58
example： B1： BLOCK
SIGNAL s1：BIT；
BEGIN
s1 <= a AND b;
B2： BLOCK
SIGNAL s2：BIT；
BEGIN
s2<= c AND d;
B3： BLOCK
BEGIN
Z <= s2;
END BLOCK B3;
END BLOCK B2;
y<= s1;
END BLOCK B1;

## Slide 59: （ⅱ）SUBPROGRAM
1．PROCEDURE
PROCEDURE format ：
PROCEDURE name（parameter list）IS
[declaration]
BEGIN
procedure statement
END PROCEDURE name；

## Slide 60
example：
PROCEDURE vector_to_int
(a: IN STD_LOGIC_VECTOR;
x_flag: OUT BOOLEAN;
q: INOUT INTEGER) IS
BEGIN
q := 0;
x_flag := FALSE;
FOR i IN a’RANGE LOOP
q := q*2;
IF (a (i) =1) THEN
q := q+1;

## Slide 61
ELSE (a (i) /=1) THEN
x_flag := TRUE;
END IF;
END LOOP;
END vector_to_int;

## Slide 62: （ⅱ）SUBPROGRAM
2.function
Function format：
FUNCTION name （ parameter list ） RETURN data type IS
[declaration]；
BEGIN
sequence statement；
RETURN [variable]；
END RETURN name ；

## Slide 63
example:
LIBRARY IEEE;
USE IEEE.STD_LOGIC_1164.ALL;
PACKAGE bpac IS
FUNCTION max (a: STD_LOGIC_VECTOR;
b: STD_LOGIC_VECTOR)
RETURN STD_LOGIC_VECTOR;
END bpac;
PACKAGE BODY bpac IS
FUNCTION max (a: STD_LOGIC_VECTOR;
b: STD_LOGIC_VECTOR)

## Slide 64
RETURN STD_LOGIC_VECTOR IS
VARIABLE tmp: STD_LOGIC_VECTOR (a’RANGE);
BEGIN
IF (a>b) THEN
tmp := a;
ELSE
tmp := b;
END IF;
RETURN tmp;
END;
END bpac;

## Slide 65: （ⅲ）PROCESS
PROCESS is used devise certain independent function circuit，it’s parallel statement 。
PROCESS format：
[lable：] PROCESS [sensitive signal list]
[declaration]；
BEGIN
< PROCESS statement >
END PROCESS [lable：]；
sequence statement

## Slide 66: The activatity of process
Have sensitive signal ： process is activated when sensitive signal change。
Have no sensitive signal ：There should have sensitivity signal stimulations in process statement， process is activated when stimulation condition fills.
WAIT、WAIT FOR、WAIT UNTILL、WAIT ON
notice： don’t allow wait statement in process statement when there has sensitivity signal.

## Slide 67: Process’synchronizing description
One architecture can have more processes ， process statement is parallel statement itself， so these processes are paralleling relation， while statements are sequential execution in one process.
LIBRARY IEEE;
USE IEEE.STD_LOGIC_1164.ALL;
USE IEEE.STD_LOGIC_UNSIGNED.ALL;
ENTITY example2 IS
PORT( clk : IN STD_LOGIC;
q : OUT STD_LOGIC);
END example2;
ARCHITECTURE a OF example2 IS
SIGNAL counter : STD_LOGIC_VECTOR(2 DOWNTO 0);
BEGIN

## Slide 68: Process’synchronizing description
count: PROCESS (clk)
BEGIN
IF (clk'EVENT AND clk='1') THEN
counter<=counter+'1';
END IF;
END PROCESS;
output: PROCESS (counter)
BEGIN
IF(counter<"101") THEN
q<='1';
ELSE
q<='0';
END IF;
END PROCESS;
END a;

## Slide 69: simulation waveform