## Slide 1: Chapter 5 Sequential circuit 'vhdl description

## Slide 2: （1） D flip-flop
LIBRARY IEEE;
USE IEEE.STD_LOGIC_1164.ALL;
ENTITY d_ff IS
PORT( clk,d : IN STD_LOGIC;
q,qd :OUT STD_LOGIC);
END d_ff;
ARCHITECTURE a OF d_ff IS
BEGIN
PROCESS(clk,d)
BEGIN
IF (clk'EVENT AND clk='1') THEN
q<=d;
qd<=NOT d;
END IF;
END PROCESS;
END a;

## Slide 3
simulation waveform

## Slide 4: DFF with asynchronous set / reset
set
reset
d
clk
q
qd
0
1
X
X
1
0
1
0
X
X
0
1
1
1
X
0
stable
stable
1
1
0
↑
0
1
1
1
1
↑
1
0

## Slide 5
LIBRARY IEEE;
USE IEEE.STD_LOGIC_1164.ALL;
ENTITY d_ffy IS
PORT( clk,d,set,reset : IN STD_LOGIC;
q,qd :OUT STD_LOGIC );
END d_ffy;
ARCHITECTURE a OF d_ffy IS
BEGIN
PROCESS(clk,set,reset)
BEGIN
IF (set='0' AND reset='1') THEN
q<='1';
qd<='0';
ELSIF (set='1' AND reset='0') THEN
q<='0';
qd<='1';
ELSIF (clk'EVENT AND clk='1') THEN
q<=d;
qd<=NOT d;
END IF;
END PROCESS;
END a;

## Slide 6
simulation waveform

## Slide 7
set
reset
d
clk
q
qd
0
1
X
↑
1
0
1
0
X
↑
0
1
1
1
X
0
stable
stable
1
1
0
↑
0
1
1
1
1
↑
1
0
DFF with synchronized set / reset

## Slide 8
LIBRARY IEEE;
USE IEEE.STD_LOGIC_1164.ALL;
ENTITY d_fft IS
PORT(clk,d,set,reset : IN STD_LOGIC;
q,qd : OUT STD_LOGIC );
END d_fft;
ARCHITECTURE a OF d_fft IS
BEGIN
PROCESS(clk,set,reset)
BEGIN
IF (clk'EVENT AND clk='1') THEN
IF (set='0' AND reset='1') THEN
q<='1';
qd<='0';
ELSIF (set='1' AND reset='0') THEN
q<='0';
qd<='1';
ELSE
q<=d;
qd<=NOT d;
END IF;
END IF;
END PROCESS;
END a;

## Slide 9
simulation waveform

## Slide 10: （2）Register
REG with asynchronous set / reset
en
set
reset
d(n)
clk
q(n)
X
0
1
X
X
1
X
1
0
X
X
0
1
1
1
X
↑
d(n)
0
1
1
X
↑
保持

## Slide 11
LIBRARY IEEE;
USE IEEE.STD_LOGIC_1164.ALL;
ENTITY registern IS
GENERIC (n:INTEGER:=1);
PORT( d : IN STD_LOGIC_VECTOR(n DOWNTO 0);
clk,en,set,reset : IN STD_LOGIC;
q : BUFFER STD_LOGIC_VECTOR(n DOWNTO 0));
END registern;
ARCHITECTURE a OF registern IS
BEGIN
PROCESS (clk,set,reset)
BEGIN
IF (set='0' AND reset='1') THEN
q<=(OTHERS=>'1');
ELSIF (set='1' AND reset='0') THEN
q<=(OTHERS=>'0');
ELSIF (clk'EVENT AND clk='1') THEN
IF (en='1' ) THEN
q<=d;
ELSE q<=q;
END IF;
END IF;
END PROCESS ;
END a;

## Slide 12
simulation waveform

## Slide 13: （3）shift register

## Slide 14: COMPONENT statement
COMPONENT <name>
[GENERIC<parameter>;]
PORT < >；
END COMPONENT;
COMPONENT d_ff
PORT( clk, d : IN STD_LOGIC;
q : OUT STD_LOGIC);
END COMPONENT;

## Slide 15: COMPonent instantiation statement
<label name>:< COMPONENT name >
[GENERIC MAP ( ) ]
PORT MAP ( );

## Slide 16: mapping method
Position map
dffx:d_ff PORT MAP(clk,d,qq(i));
dffx:d_ff PORT MAP(clk=>clk,d=>d,q=>q(i));
Name map

## Slide 17: GENERATE
[Lable：] < > GENERATE
< >；
END GENERATE;

## Slide 18
[lable：] FOR i IN range GENERATE
< >；
END GENERATE [lable]；
[lable ：] IF 〈condition〉 GENERATE
〈〉;
END GENERATE[lable];
FOR
IF
g1: IF(i=0) GENERATE
dffx:d_ff PORT MAP(clk,d,qq(i));
END GENERATE g1;

## Slide 19
LIBRARY IEEE;
USE IEEE.STD_LOGIC_1164.ALL;
ENTITY shiftn IS
GENERIC (n:INTEGER:=2);
PORT( d,clk: IN STD_LOGIC;
q : OUT STD_LOGIC);
END shiftn;
ARCHITECTURE a OF shiftn IS
COMPONENT d_ff
PORT( clk, d : IN STD_LOGIC;
q : OUT STD_LOGIC);
END COMPONENT;
SIGNAL qq : STD_LOGIC_VECTOR(0 TO n);
BEGIN
q<=qq(n);
label1: FOR i IN 0 TO n GENERATE
g1: IF(i=0) GENERATE
dffx:d_ff PORT MAP(clk,d,qq(i));
END GENERATE g1;
g2: IF(i/=0) GENERATE
dffx:d_ff PORT MAP(clk,qq(i-1),qq(i));
END GENERATE g2;
END GENERATE label1;
END a;

## Slide 20
ARCHITECTURE aa OF shiftn IS
SIGNAL tmp : STD_LOGIC_VECTOR(0 TO n);
BEGIN
q<=tmp(n);
PROCESS(clk)
BEGIN
IF(clk'EVENT AND clk='1') THEN
tmp(0)<=d;
FOR i IN 1 TO n LOOP
tmp(i)<=tmp(i-1);
END LOOP ;
END IF;
END PROCESS;
END aa;

## Slide 21
simulation waveform

## Slide 23
LIBRARY IEEE;
USE IEEE.STD_LOGIC_1164.ALL;
ENTITY shiftb IS
GENERIC (n:INTEGER:=2);
PORT( d,clk: IN STD_LOGIC;
q : BUFFER STD_LOGIC_VECTOR(0 TO n));
END shiftb;
ARCHITECTURE a OF shiftb IS
COMPONENT d_ff
PORT( clk, d: IN STD_LOGIC;
q : OUT STD_LOGIC);
END COMPONENT;
BEGIN
label1: FOR i IN 0 TO n GENERATE
g1: IF(i=0) GENERATE
dffx:d_ff PORT MAP(clk=>clk,d=>d,q=>q(i));
END GENERATE;
g2: IF(i/=0) GENERATE
dffx:d_ff PORT MAP(clk=>clk,d=>q(i-1),q=>q(i));
END GENERATE;
END GENERATE ;
END a;

## Slide 24
ARCHITECTURE aa OF shiftb IS
BEGIN
PROCESS(clk)
BEGIN
IF(clk'EVENT AND clk='1') THEN
q(0)<=d;
FOR i IN 1 TO n LOOP
q(i)<=q(i-1);
END LOOP ;
END IF;
END PROCESS;
END aa;

## Slide 25
simulation waveform

## Slide 26: Reentrant shift register
LIBRARY IEEE;
USE IEEE.STD_LOGIC_1164.ALL;
ENTITY shiftx IS
PORT( clk,load : IN STD_LOGIC;
d : IN STD_LOGIC_VECTOR(3 DOWNTO 0);
q : OUT STD_LOGIC_VECTOR(3 DOWNTO 0));
END shiftx;

## Slide 27
ARCHITECTURE aa OF shiftx IS
SIGNAL tmp : STD_LOGIC_VECTOR(3 DOWNTO 0);
BEGIN
q<=tmp;
PROCESS(clk)
BEGIN
IF(clk'EVENT AND clk='1') THEN
IF(load='0') THEN
tmp<=d;
ELSE tmp(0)<=tmp(3);
tmp(3 downto 1)<=tmp(2 downto 0);
END IF;
END IF;
END PROCESS;
END aa;

## Slide 28
simulation waveform

## Slide 29: （4）COUNTER
Synchronous up_down counter
LIBRARY IEEE;
USE IEEE.STD_LOGIC_1164.ALL;
USE IEEE.STD_LOGIC_UNSIGNED.ALL;
ENTITY updowncounter IS
PORT( clk, updown : IN STD_LOGIC;
q:OUT STD_LOGIC_VECTOR(2 DOWNTO 0));
END updowncounter;

## Slide 30
ARCHITECTURE a OF updowncounter IS
SIGNAL counter : STD_LOGIC_VECTOR(2 DOWNTO 0);
BEGIN
q<=counter;
PROCESS(clk)
BEGIN
IF (clk'EVENT AND clk='1') THEN
IF(updown='1') THEN
counter<=counter+'1';
ELSE counter<=counter-'1';
END IF;
END IF;
END PROCESS;
END a;

## Slide 31
simulation waveform

## Slide 32: Asynchronous counter
LIBRARY IEEE;
USE IEEE.STD_LOGIC_1164.ALL;
ENTITY d_ffr IS
PORT( clk,d,clr : IN STD_LOGIC;
q,qd : OUT STD_LOGIC );
END d_ffr;
ARCHITECTURE a OF d_ffr IS
BEGIN
PROCESS(clk,clr)
BEGIN
IF (clr='0') THEN
q<='0';
qd<='1';
ELSIF (clk'EVENT AND clk='1') THEN
q<=d;
qd<=NOT d;
END IF;
END PROCESS;
END a;

## Slide 33
simulation waveform

## Slide 35
LIBRARY IEEE;
USE IEEE.STD_LOGIC_1164.ALL;
ENTITY acounter IS
PORT( clk,reset: IN STD_LOGIC;
q : OUT STD_LOGIC_VECTOR(2 DOWNTO 0));
END acounter;
ARCHITECTURE a OF acounter IS
COMPONENT d_ffr
PORT( clk, d,clr: IN STD_LOGIC;
q,qd : OUT STD_LOGIC);
END COMPONENT;
SIGNAL tmp : STD_LOGIC_VECTOR(3 DOWNTO 0);
BEGIN
tmp(0)<=clk;
label1: FOR i IN 0 TO 2 GENERATE
dffrx : d_ffr PORT MAP( clk=>tmp(i),
d=>tmp(i+1),
clr=>reset,
q=>q(i),
qd=> tmp(i+1));
END GENERATE label1;
END a;

## Slide 36
simulation waveform

## Slide 37: （5）Frequency Divider
LIBRARY IEEE;
USE IEEE.STD_LOGIC_1164.ALL;
USE IEEE.STD_LOGIC_UNSIGNED.ALL;
ENTITY clk_div IS
PORT(clk : IN STD_LOGIC;
q : BUFFER STD_LOGIC);
END clk_div;
ARCHITECTURE a OF clk_div IS
SIGNAL counter : STD_LOGIC_VECTOR(1 DOWNTO 0);
BEGIN
PROCESS(clk)
BEGIN
IF (clk'EVENT AND clk='1') THEN
IF(counter="10") THEN
counter<="00";
q<=NOT q;
ELSE
counter<=counter+'1';
END IF;
END IF;
END PROCESS;
END a;

## Slide 39
LIBRARY IEEE;
USE IEEE.STD_LOGIC_1164.ALL;
USE IEEE.STD_LOGIC_UNSIGNED.ALL;
ENTITY clk_div8 IS
PORT( clk : IN STD_LOGIC;
q : BUFFER STD_LOGIC);
END clk_div8;
ARCHITECTURE a OF clk_div8 IS
SIGNAL counter : STD_LOGIC_VECTOR(2 DOWNTO 0);
BEGIN
PROCESS(clk)
BEGIN
IF (clk'EVENT AND clk='1') THEN
IF(counter="010") THEN
counter<=counter+'1';
q<=NOT q;
ELSIF(counter="111") THEN
counter<="000";
q<=NOT q;
ELSE
counter<=counter+'1';
END IF;
END IF;
END PROCESS;
END a;

## Slide 40
simulation waveform

## Slide 41: (6)、Tristate gate
LIBRARY IEEE;
USE IEEE.STD_LOGIC_1164.ALL;
ENTITY tri_gate IS
PORT( din,en : IN STD_LOGIC;
dout : OUT STD_LOGIC);
END tri_gate;
ARCHITECTURE a OF tri_gate IS
BEGIN
PROCESS(en,din)
BEGIN
IF (en='1') THEN
dout<=din;
ELSE
dout<='Z';
END IF;
END PROCESS;
END a;

## Slide 42
Z
simulation waveform

## Slide 43: （7） Tristate Buffer
LIBRARY IEEE;
USE IEEE.STD_LOGIC_1164.ALL;
ENTITY tri_buff4 IS
PORT( en : IN STD_LOGIC;
din : IN STD_LOGIC_VECTOR(3 DOWNTO 0);
dout : OUT STD_LOGIC_VECTOR(3 DOWNTO 0));
END tri_buff4;
ARCHITECTURE a OF tri_buff4 IS
BEGIN
PROCESS(en,din)
BEGIN
IF (en='1') THEN
dout<=din;
ELSE
dout<="ZZZZ";
END IF;
END PROCESS;
END a;

## Slide 44
Z
simulation waveform